## Slide 1: Improving Pedestrian and Bicycle Safety and Accessibility: Short-term and Long-term Strategies
Arlington, Virginia
Road to Zero Coalition Meeting
Dan Nabors, P.E. December 12, 2017

## Slide 2: Arlington County Background
Notes: 25.8 sq. miles
11 Metrorail stations
Frequently investigate citizen, Civic Association, and Planning Dept requests to mark crosswalks at unmarked crossings

## Slide 3: Pedestrian and Bicycle Projects
Capital Projects
Long-Range
Transportation & Redevelopment
Safety Reviews
Corridors
Hot Spots
Community
Input
Engagement
Repaving, Remarking, & Signage Reviews
Maintenance
Short-range
Crossings Overview
2,800 intersections
300 signalized intersections
1,100 transit stops
8 Pedestrian Hybrid Beacons
Bicycle Lanes Overview
Extensive trail network
Over 75 miles of on-street lanes
Time

## Slide 4: Pavement Marking Process
Review Data
Review crash data
Review traffic data
Coord. w/ Signals
Confirm traffic control
Notify staff of paving limits (coordinate loop replacement on signals)
Coord. w/ Transit
Obtain bus stop ridership
Analyze location of stops
Coord. w/ Planning
Engineer Review
Coordinate ped/bike master plan/CIP improvements
Obtain data if necessary and analyze location of crossings
Review data and analysis
Approve plans
CADD Standards
Design Standards
Design Process

## Slide 5
Increase Effectiveness Of Crosswalks With:
High Visibility Markings
Signing
Curb Extensions
Notes: Physical treatments such as these listed do the most to improve pedestrian safety at crosswalks. They will be covered in greater detail in the rest of this module.

## Slide 6: Improve Crosswalk Visibility
2-lane roads- high visibility markings
In-street pedestrian volumes based on volume, speed, and geometry

## Slide 7: Apply Additional Markings
Use MUTCD as minimum standard
Other markings as needed to standardize lanes
Provide additional guidance to motorists

## Slide 8: Improve Effectiveness of Bike Lanes with:
Buffered bike lanes
Standardize cross section with application of buffered bike lanes
2-lane roads- high visibility crosswalk markings

## Slide 9: Improve Effectiveness of Bike Lanes with:
Buffered bike lanes
Standardize cross section with application of buffered bike lanes
2-lane roads- high visibility crosswalk markings

## Slide 10: Improve Effectiveness of Bike Lanes with:
Protected bike lanes
Standardize cross section with application of protected bike lanes
Look at maintenance impacts

## Slide 11: Additional Measures
Other markings as needed to standardize lanes
Reallocate space

## Slide 12: Improve Signage
Pedestrian Hybrid Beacon

## Slide 13
Better visibility
Traffic calming
Room for pedestrians
Other advantages
Curb extensions
Reduce crossing distance
Notes: Animated. Self-explanatory except last point: once the curb extension is in place, parking can be moved closer to the crosswalk.

## Slide 14
Curb extensions
Reduce crossing distance
Better visibility
Traffic calming
Room for pedestrians
Other advantages
Notes: Animated. Self-explanatory except last point: once the curb extension is in place, parking can be moved closer to the crosswalk.

## Slide 15: Corridor Projects
Medians do not provide refuge
Wide intersection
Skewed crossing

## Slide 16: Corridor Projects
Median refuge
Shorter crossing
Smaller intersection footprint
Bioretention facilities

## Slide 17: Median Refuge- Spot Location
Median refuge
Small island
RRFB
Bulb outs
High visibility markings

## Slide 18: Median Refuge- Spot Location
Median refuge
Small island
RRFB
Bulb outs
High visibility markings

## Slide 19: Median Refuge- Spot Location
Median refuge
Small island
RRFB
Bulb outs
High visibility markings

## Slide 20: Short-Range Median Improvements
Opportunistic
High traffic areas
Vulnerable users
Wide lanes
With repaving or stand-alone marking projects

## Slide 21: Short-Range Median Improvements
Pilot
Collect before and after data
Make adjustments
Update design guidance
Continue implementation

## Slide 22: Short-Range Median Improvements

## Slide 23: Short-Range Median Improvements

## Slide 24: Short-Range Median Improvements

## Slide 25: Short-Range Median Improvements
Stage 1
Markings
Signage
Bollards

## Slide 26: Short-Range Median Improvements
Stage 2
Planters and physical separation added
Final design will include hardscape curb and gutter changes

## Slide 27: Existing Street

## Slide 28: Short-Range Improvements

## Slide 29: Long-Range Improvements

## Slide 30: Road Diet- Wilson Blvd
2015 - Year 1
Repaving and restriping from four lanes to three lanes
Providing a center left turn lane throughout
Addition of bike lanes on both sides
Bus stop consolidation
2016 – Year 2
Began monitoring the reconfiguration and collected data on traffic flow and safety.
2017 – Year 3
Extended road diet one block.
Notes: of the demonstration project. The goals of the reconfiguration were to improve pedestrian, cyclist, and motorist safety, to better accommodate all road users

## Slide 31: Road Diet- Wilson Blvd
https://projects.arlingtonva.us/projects/wilson-boulevard-improvements/
Road diet extension
Crossing
First Phase of Road Diet: 3,600 Ft.
First Phase of Road Diet: 3,600 Ft.

## Slide 32: Road Diet- Wilson Blvd
https://projects.arlingtonva.us/projects/wilson-boulevard-improvements/

## Slide 33: Dan Nabors, P.E. Arlington County DES Transportation Engineering & Operations O: 703-228-3726 dnabors@arlingtonva.us