## Slide 1
Fundamentals of Industrial Hygiene 6th Edition
Chapter 17:
Direct-Reading Instruments
for Gases, Vapors, and
Particulates
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
Identify and/or quantify the concentration of many gases, vapors, and particulates in air—in real-time or near real-time.
May be used to quickly assess the exposure of workers to hazardous chemicals.
    level 1 (small, hand-held, simple)
    level 2 (small, hand-held)
    level 3 (person-portable)
    level 4 (transportable)

## Slide 3: Common Types of Instruments
General Types
  compound-specific monitors (single compound)
  non-specific monitors (leak detectors, known contaminant)
  broad-range monitors (multiple compounds)

## Slide 4: Common Types of Instruments (cont.)
Specific Types
  combustible gas/multiple gas (combustible gas (LEL), O2, CO, H2S)
  explosive (flammable) limits
  indoor air quality monitors (temp., relative humidity, CO2, other gas)
  particle counters (obscuration, deposition, condensation nuclei)

## Slide 5: Flammable Gas Meter Concerns
instrument design
  must be intrinsically safe for use with flammable gases
zero adjustment
  contaminant free area
  purified air
interpretations of meter readings
  low vapor pressure liquids
  high vapor pressure liquids
  catalyst poisoning
  interferences

## Slide 6: Sensing Technologies
A variety of direct-reading instruments are available:
  catalytic combustible gas sensors
  electrochemical detectors
  thermal conductivity detectors
  flame ionization detectors
  photoionization detectors
  solid state resistors
  photo-acoustic spectrometers
  surface acoustic wave detectors
  electron capture detectors

## Slide 7: Sensing Technologies (cont.)
colorimetric
  detector tubes (short- and long-term, active and passive)
  badges
  glove breakthrough indicators
  tape samplers (levels, durations, and time of exposures)
potential issues with colorimetric devices
  interpreting results (stain fade, ability to read)
  specificity (interferences, reaction rates)
  shelf life

## Slide 8: Calibration
All direct-reading instruments must be calibrated before use, and at intervals during use.
An instrument’s response to a concentration of a substance can shift as a result of:
    chemical degradation of sensors
    physical damage
    drift in electronic components
    exposure to extreme environmental conditions (temp., humidity)
    extremely high contaminant exposures
    exposures to poisons or inhibitors
  Note: Do not confuse calibration with zeroing-out.

## Slide 9: Calibration (cont.)
Full calibration
  use cylinders filled with a known concentration of a gas
Functional calibration/bump test
  briefly expose instrument to a concentration above the instrument’s lowest alarm set point