## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Chapter 16:
Air Sampling
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
When evaluating and controlling inhalation hazards, industrial hygienists typically compare the measured concentration of an airborne chemical to a recognized exposure limit.
Standardized methods for collection of air samples have been developed.

## Slide 3: Types of Air Samples
Air sampling is used to:
  evaluate employee exposure
  assist in design and evaluation of control measures
  document compliance with regulations
personal vs. area sampling
grab vs. integrated sampling

## Slide 4: Air-Sampling Equipment
Two categories of air-sampling equipment:
  direct-reading instruments
  sample collection devices
Sampling train
    suction pump
    air inlet orifice
    collection device
    flow-rate control device
    airflow meter

## Slide 5: Collection Devices for Gases/Vapors
A substance is considered a gas if this is its normal physical state under conditions of standard temperature (70°F) and pressure (14.7 psi).
gases and vapors behave similarly:
    follow the ideal gas laws
    do not stratify based on densities
  grab sampling
    evacuated canisters, gas-sampling bag
    advantages
    disadvantages

## Slide 6: Collection Devices for Gases/Vapors (cont.)
  integrated sampling
    absorption
      gas wash bottles
      fritted tube impingers
    adsorption
      activated charcoal tubes
        breakthrough
      silica gel tubes

## Slide 7: Collection Devices for Gases/Vapors (cont.)
  diffusion (passive) samplers
    allow personal monitoring
    inexpensive
    easy to use
    accurate
    can provide quick feedback
  colorimetric passive monitors

## Slide 8: Collection Devices for Particulates
Airborne particulates can be solid, liquid, or both, and can range in size from visible to microscopic.
  several types of collection media
    glass, cellulose, polyvinyl chloride fibers
  filters
    filter overloading
    particle sizing
      inhalable
      thoracic
      respirable
  cyclones
  inertial impactors

## Slide 9: Suction Pumps
Responsible for moving air through a sampling train.
Must be listed by UL or equivalent as intrinsically safe if used in flammable/explosive atmospheres.
three types
low flow (5–500 mL/min)
high flow (0.5–15 L/min)
dual range

## Slide 10: Flow-Rate Meters
Maintaining a constant air flow rate through the sampling train is critical.
pressure-compensating devices
critical-flow orifices

## Slide 11: Selecting Sampling Methods
The selection of a sampling method depends on:
sampling objective
physical and chemical characteristics of contaminant
presence of other chemicals
required accuracy and precision
regulatory requirements
portability and ease of use
cost
reliability
type of sampling needed
duration of sampling
    NIOSH: Manual of Analytical Methods
    OSHA: Sampling and Analytical Methods

## Slide 12: Selecting Sampling Methods (cont.)
Critical considerations regarding sampling include:
sample media
  special handling requirements
flow rate
  obtain an adequate sample
  prevent breakthrough
sample duration
  requirements to obtain an adequate sample

## Slide 13: Calibration
The suction pumps used for air sampling must be calibrated to the airflow recommended in the sampling methodology.
  primary calibration
    wet process
    dry process
    mass flow sensors
  secondary calibration
    rotameters

## Slide 14: Sampling and Analytical Error
After analysis and calculation of time-weighted averages, the sampling and analytical error (SAE) must be determined.
SAE = [(airflow error)2 + (time error)2 + (analytical error)2]1/2
  airflow error
  time error
  analytical error

## Slide 15: Record Keeping
    Complete and detailed records must be kept on:
  sampling procedures
    conducted according to accepted professional standards
    identity of equipment used
    calibration procedures and results
    identity of analytical lab and related lab reports
    air-sampling calculations
  sampling conditions
  sampling results
  29 CFR 1910.20 Access to Employee Exposure and Medical Records
    generally, exposure standards must be kept for 30 years
    must be readily available to employees and their representatives