## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Part V: Control of Hazards
Chapter 18:
Methods of Control
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
The types of industrial hygiene control measures to be instituted depend on:
  the nature of the substance
  its route(s) of entry
    traditional industrial settings
    non-traditional workplaces
  To lower exposures, the industrial hygienist must determine:
    the contaminant source
    the path it travels to the worker
    the employee’s work pattern and use of PPE

## Slide 3: Methods of Control
Engineering controls
  remove or reduce the hazard
    ventilation
    isolation
    substitution
Administrative controls
  minimize workers’ exposure
    scheduling reduced work times
    good work practices
    training
Personal protective equipment
  last line of defense

## Slide 4: Engineering Controls at Design Stage
The best time to introduce engineering controls is when facility is in its design phase, because controls can be:
  integrated more readily
  reconciled with regulations
  less costly than retrofitting
    design so airborne contaminants are kept below OELs
    isolate process equipment and vent to a collector/incinerator
    remotely control process from a protected room
  accumulation
  concurrent activities

## Slide 5: Design
  In processes where toxic, reactive, flammable, or explosive chemicals are involved, OSHA requires a process hazard analysis (29 CFR 1910.19).
  Design factors to be addressed include:
    can hazardous residues be removed before equipment is opened?
    how can system be designed to be maintenance-free?
    can a closed-system be used?
    can process be conducted automatically (no worker involvement)?
    can system be cleaned automatically?
    what precautions can be taken to prevent/detect unplanned releases?

## Slide 6: Design (cont.)
  When air contaminants are created, generated, or released in concentrations that can injure, ventilation is the usual method of control.
  Design factors to be addressed include:
    has building been designed to effectively control moisture?
    is fresh air intake located away from contaminant source?
    can HVAC system deliver an appropriate volume of air?
    is local exhaust ventilation required in any special-use areas?
    are special filters required?
    if smoking is permitted, is it located away from doors, windows, etc.?

## Slide 7: Maintenance
Untoward events leading to the release of contaminants fall into two general classes:
  continuous leaks
    low-level background exposures
    becomes more serious as equipment wears
  momentary openings
    brief, high-level exposures
    adjustments, lubrication, cleaning
    sampling
    filter replacement

## Slide 8: Hazardous Materials
  Some materials must be handled carefully because of their toxicity, flammability, corrosiveness, or reactivity.
  Federal codes (OSHA and others) impose stringent controls regulating:
    mutual process proximity
    ventilation
    sources of ignition
    facility/process design

## Slide 9: Industrial Hygiene Control Measures
Industrial hygiene control methods include:
  engineering controls
    substitution
    change or alteration of the process
    isolation or enclosure of process or operation
    local exhaust ventilation
    general (dilution) ventilation
    shielding
  administrative controls
    good housekeeping and maintenance
    wet work-methods
    employee training ( including emergency response training)
    waste treatment and disposal
    continuous monitoring (with pre-set alarms)
  personal protective equipment

## Slide 10: Principles of Engineering Controls
Substitution
  changing the material (e.g., less toxic or non-toxic for a highly toxic)
  changing the process (e.g., reduce dust/fume dispersion)
Isolation
  physical barrier (e.g., acoustic panels)
  time (e.g., remote control equipment)
  separation (e.g., isolating hazardous operations from other work areas)
  containment (e.g., isolate hazardous materials in airtight enclosures)
  scheduling (minimize number of workers exposed . . . mine blasting)
Ventilation
  general ventilation (dilute contaminants)
  local exhaust ventilation (capture and remove contaminants)

## Slide 11: Principles of Engineering Controls (cont.)
Shielding
  eliminate exposures to physical hazards
    heat (reflective panels)
    ionizing radiation (lead or concrete walls)
    non-ionizing radiation (Faraday cages, grounding)
    noise (acoustical barriers)

## Slide 12: Principles of Administrative Controls
Reduction of work periods
  use caution (exposes more workers to the hazard)
  Note: Not permitted by certain OSHA standards for highly
  toxic materials (e.g., asbestos).
Wet-work methods
  wetting to control dust
  may need to add surfactants
Housekeeping
  often mandated by OSHA standards
    remove dust on overhead ledges and floors (re-suspension)
    immediate cleanup of spills
    all absorbents placed in airtight receptacles and emptied daily

## Slide 13: Principles of Administrative Controls (cont.)
Personal hygiene
  provision of hand-washing facilities, showers, eyewash stations
  prohibition of using compressed air
    re-suspends contaminant
    may cause hearing damage
    can result in physical injury
    may result in injection
  prohibition on eating, drinking, or food storage in areas where toxic materials are used

## Slide 14: Maintenance Provisions
Large-scale, periodic equipment and process shutdown typically results in employees from many crafts working to clean and repair equipment.
  anticipate exposure of all workers to contaminants
  clean equipment/piping systems before dismantling
  implement short-term exposure controls before disassembly
  decontaminate equipment, tools, and PPE before removal from worksite
  conduct air monitoring

## Slide 15: Waste Disposal
Most wastes are regulated by complex requirements of federal, state, and local agencies.
  Development of an appropriate waste-management plan requires employers to determine:
    are potentially regulated wastes generated on-site?
    have wastes been tested to determine their characteristics?
    what types of wastes are generated (e.g., hazardous, toxic, infectious)?
    can wastes be treated and rendered safe prior to disposal?
    can wastes be recycled?
    what quantities of wastes are generated (i.e., small-quantity vs. large-quantity generator)
    is facility a waste generator, transporter, or treatment-storage-disposal facility (TSDF).