## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Chapter 22:
Respiratory Protection
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
If the work environment is still not completely safe after engineering and administrative controls have been implemented, it will be necessary to use respirators.
OSHA has established 29 CFR 1910.134: Respiratory Protection, for regulating the use of respiratory-protective equipment.
  Respirators are the least satisfactory means of exposure control:
    some employees may not be able to wear a respirator;
    respirators can be cumbersome to use and hot to wear
    respirators may reduce vision and interfere with communication

## Slide 3: Respiratory Protection Programs
29 CFR 1910.134 requires a written program be developed when respiratory protection is required.
Should include worksite-specific procedures covering:
    exposure assessment;
    proper selection of equipment;
    medical evaluation of respirator wearers;
    fit testing of workers;
    proper respirator use (routine, emergency, and rescue operations);
    schedules (cleaning, storing, inspection, repairing, and discarding);
    regular program evaluation.

## Slide 4: Respiratory Protection Programs (cont.)
Worksite-specific procedures
  procedures must cover each element in enough detail so it is clear exactly how each element will be accomplished
  should include disciplinary policies regarding failure to use respirators and facial hair
Exposure assessment
  identify the need for respirators
  identify the level of protection required
  establish required change schedule for chemical cartridge respirators

## Slide 5: Respiratory Protection Programs (cont.)
Proper selection
  hazard to which worker is exposed
  exposure assessment
  relevant workplace and use factors
Medical evaluation
  physiological stresses associated with respirator use
    type of respirator (types and weights)
    job/task being performed (work activities, physical effort, duration)
    workplace conditions (additional PPE, environmental conditions)

## Slide 6: Respiratory Protection Programs (cont.)
Respirator fit
  workers using tight-fitting respirators must be fit tested
Respirator use
  respirator wearers must check seal before entering harmful atmospheres
  not a substitute for a qualitative or quantitative fit test

## Slide 7: Respiratory Protection Programs (cont.)
Training
  upon initial assignment
  annual retraining
  retrain when:
    changes in workplace or respirator type
    inadequacies in worker knowledge or use of respirator
    any other situation where retraining appears necessary
  wearer must be able to demonstrate
    why respirator is necessary
    limitations and capabilities of respirator
    how to use respirator in emergency situations
    to to inspect, don & doff, use, and check seals
      Note: Must include an opportunity for each wearer to handle the respirator and include demonstrations and practice.
    how to recognize signs and symptoms that may prevent respirator use
    general requirements of the OSHA standard

## Slide 8: Respiratory Protection Programs (cont.)
Respirator maintenance
  cleaning and disinfecting
  inspection for defects
  proper storage
Exposure assessment
  identify the need for respirators
  identify the level of protection required
  establish required change schedule for chemical cartridge respirators

## Slide 9: Respiratory Program Administration
Responsibility for program must be assigned to one person who may have the assistance of others.
  must have sufficient knowledge of:
    current issue
    advances in technology
    regulatory changes
  responsibilities include:
    conducting exposure assessments
    selecting appropriate respirators
    maintaining records and written procedures
    evaluating program effectiveness (ongoing surveillance)

## Slide 10: Classes of Respirators
Respiratory-protective devices can be categorized into three classes based on the capabilities and limitations:
  air-purifying devices
  atmosphere-supplying devices
  combination air-purifying and atmosphere supplying devices
HVAC systems also provide for odor control and maintenance of oxygen and carbon dioxide levels.

## Slide 11: Air-Purifying Devices
Function to cleanse the contaminated atmosphere before breathing.
limited to use in atmospheres containing sufficient oxygen and contaminant level is within devices ability to cleanse
  useful life is limited:
    concentration of contaminants
    breathing rate of wearer
    temperature and humidity levels in workplace
    removal capacity of air-purifying medium
    aerosol-removing respirators
    gas/vapor-removing respirators
    combination
    powered air-purifying respirators (PAPRs)

## Slide 12: Aerosol-Removing Respirators
  Offer protection against airborne particulate matter, but do not protect against gases, vapors, and oxygen deficiency
  nine classes of filter respirators allowed:
    type of aerosol
      N-series
      R-series
      P-series
    filter efficiency
      95%
      99%
      99.97%

## Slide 13: Gas/Vapor-Removing Respirators
Protect against certain gases and vapors by using various chemical filters
  adsorption
  chemosorption
  service life depends on several factors:
    high contaminant concentrations
    high breathing rate
    high humidity levels

## Slide 14: Atmosphere-Supplying Respirators
Provide a respirable atmosphere to wearer independent of ambient air.
  air-line respirators (non-IDLH atmospheres only)
    demand mode (negative pressure on inhalation)
    pressure mode (positive pressure at all times
    continuous flow (used where ample air supply is available)
  self-contained breathing apparatus (SCBA) respirators
    closed-circuit
    open-circuit
  combination air-line and SCBA respirators
    primary airline
    auxillary SCBA
      ≤ 10-minute (escape only)
      > 15-minute (emergency entry)

## Slide 15: Combination Air-Purifying and Atmosphere-Supplying Devices
Can be used in either air-purifying or air-line mode.
  limitations include
    cannot be used in IDLH atmospheres
    cannot be used in oxygen-deficient atmospheres
    must use hose lengths and pressure ranges specified by manufacturer
    can only be used in atmospheres for which the air-purifying element is approved

## Slide 16: Respirator Selection
  Proper selection starts with an assessment of the inhalation hazards present in the workplace.
  29 CFR 1910.134 states that respirators shall be selected on the basis of respiratory hazard(s) in the workplace and relevant workplace and user factors:
    nature of hazardous operation or process
    type of respiratory hazard
    location of hazardous area (in relation to nearest respirable air source)
    time period respirators must be worn
    worker activities

## Slide 17: Hazard Determination
  The steps for hazard determination are:
    If the potential for an oxygen-deficient atmosphere exists, measure the oxygen level.
    Determine what contaminant(s) may be present.
    Determine if any OELs exist for the contaminant(s).
    Determine if any IDLH concentrations for contaminant(s) exist.
    Measure the concentration of the contaminant(s).
    Determine if the contaminant(s) can be absorbed through the skin, cause skin irritation, or be irritating or corrosive to the eyes or skin.
    For gases/vapors, determine if there is a known taste, odor, or irritation threshold.

## Slide 18: Warning Properties
  Warning properties rely on human senses, and those senses are not foolproof.
  variation of odor threshold of general population
    (two orders of magnitude)
  shift in odor threshold
    (caused by extended exposure to low concentrations)
  shifts in odor threshold
    (caused by simple colds or other illnesses)
  failure to notice odors
    (distractions in workplace)

## Slide 19: Immediately Dangerous to Life and Health
  Numerous definitions have been presented, but the common theme is that exposure to IDLH atmospheres would affect workers acutely as opposed to chronically.
  OHSA defines IDLH as an atmosphere that:
    poses an immediate threat to life
    would cause irreversible adverse health effects
    would impair an individual’s ability to escape
      Note: The only two devices that can be used in IDLH atmospheres are the full facepiece pressure-demand SCBA (minimum 30 minutes) and the combination full facepiece air-line with auxiliary SCBA (minimum 10-minute).

## Slide 20: Assigned Protection Factors
  The expected workplace level of respiratory protection provided by a properly functioning respirator that was properly fitted to a trained user.
  Established by OSHA (see Table 22-G in text).
  Note: An APF of 10 means the respirator will reduce the concentration of contaminant actually breathed by the worker by 10 times compared to actual airborne contamination.

## Slide 21: Change Schedules
  Unless the cartridge has an end-of-service indicator built in, the only method available for replacing cartridges before breakthrough is by a cartridge change schedule.
  Unless OSHA has established a change schedule, a documented, pre-determined interval must be established based on:
    specific respirator and cartridge to be used
    airborne concentration of contaminant(s)
    temperature and humidity in workplace
    pattern of respirator use (hours/shift, shifts/week)
    expected work rate

## Slide 22: Respirator Selection Steps
if atmosphere is oxygen-deficient
    a respirator approved for IDLH atmospheres must be selected
if potential contaminant(s) could not be identified
    a respirator approved for IDLH atmospheres must be selected
if no OEL is available and estimates of toxicity cannot be determined
    a respirator approved for IDLH atmospheres must be selected
if concentration of contaminant(s) exceed published IDLH
    a respirator approved for IDLH atmospheres must be selected

## Slide 23: Respirator Selection Steps (cont.)
divide the contaminant concentration by the exposure limit to obtain a hazard ratio
if substance-specific standards exist for the contaminant(s), consider those guidelines
if more than one contaminant is present, consider potential additive/synergistic effects
    use the ACGIH TLV for mixtures
    select a filter with an APF greater than the hazard ratio

## Slide 24: Respirator Selection Steps (cont.)
if contaminant(s) is an particle
  a respirator with a particulate filter must be selected
    proper series (N, R, P)
    proper efficiency (95%, 99%, 99.97%)
if contaminant is a gas/vapor
  a respirator with an effective cartridge must be selected
  establish a change schedule

## Slide 25: Respirator Fit Testing
Proper protection will not be provided if the respirator facepiece does not fit the wearer properly.
All tight-fitting (half- and full-facepiece) respirators (whether positive or negative pressure) must be fit tested.
  qualitative fit testing
    relies on wearer’s subjective response to detection of a test agent
  quantitative fit testing
    measures for actual leakage of a test agent