## Slide 1: CHAPTER 9
Respiratory Protection

## Slide 2: Learning Objectives
List Occupational Safety and Health Administration (OSHA) requirements for respiratory protection.
Describe basic human anatomy and function of the lungs.
Outline the requirements for medical clearance needed prior to wearing a respirator.
Understand how respirators work and the different types available.
Review the respirator fit-testing purpose and process.

## Slide 3: OSHA 29 CFR 1910.134 Respiratory Protection
Used in general industry
When engineering controls are not feasible, employers must provide appropriate PPE.

## Slide 4: Written Programs
Must include:
  procedures for selecting respirators
  medical evaluation of employees using respirators
  fit-testing of respirators
  procedures for proper use of respirators
  procedures for cleaning and disinfecting respirators
  procedures for air quality in using air-supplied respirators
  training and training procedures
  evaluating the effectiveness of the respiratory protection program
  procedures where respirators are not required

## Slide 5
Source: Blausen.com staff. Blausen gallery 2014. Wikiversity Journal of Medicine.
Respiratory System

## Slide 6: Inertial Impaction

## Slide 7: Interception

## Slide 8: Sedimentation

## Slide 9: Diffusion/Brownian Motion

## Slide 10: Electrostatic Precipitation

## Slide 11: N-Series Filters
N95 particulate filter—at least 95% efficient
N99 (previously low efficiency) particulate filter—at least 99% efficient
N100 (previously high efficiency) particulate filter—at least 99.97% efficient

## Slide 12: R-Series Filters
R95 particulate filter—at least 95% efficient
R99 (previously low efficiency) particulate filter—at least 99% efficient
R100 (previously high efficiency) particulate filter—at least 99.97% efficient

## Slide 13: P-Series Filters
P95 particulate filter—at least 95% efficient
P99 (previously low efficiency) particulate filter—at least 99% efficient
P100 (previously high efficiency) particulate filter—at least 99.97% efficient

## Slide 14: Vapor and Gas Removal Mechanisms
Adsorption
Absorption
Catalyst

## Slide 15: Air-Purifying Respirators
Source: Used with permission from MSA.
Source: Used with permission from MSA.

## Slide 16: Air-Purifying Respirators (cont.)
Disposable air-purifying respirators
Reusable quarter-face, half-face, or full-face Respirators
Mouthpiece respirator

## Slide 17: Air-Purifying Respirators (Cont.)
Powered air-purifying respirator (PAPR)
Source: Used with permission from MSA.

## Slide 18: Atmosphere-Supplying Respirators
Self-contained breathing apparatus
Air-line respirators
Source: Used with permission from MSA.

## Slide 19
Assigned Protection Factors

## Slide 20: Medical Evaluation
Evaluations determine
  limitations of respirator use by the worker
  additional or follow-up medical evaluations
  that the worker can use the type of respirator being provided by the employer
  that the employer must provide an additional type of respirator
  whether the employee is medically fit to use a respirator

## Slide 21: Fit-Testing Procedures
Qualitative fit-testing
Source: Used with permission from MSA.
Source: Used with permission from MSA.

## Slide 22: Fit-Testing Procedures (cont.)
Quantitative fit-testing
Source: Used with permission from MSA.

## Slide 23: Fit-Testing Procedures (cont.)
Normal breathing
Deep breathing
Turning head side to side
Moving head up and down
Talking (reciting the rainbow passage)
Grimace (making faces)
Bending over or jogging in place
Normal breathing