# Supervisors' Safety Manual, Tenth Edition

# Chapter 1414: Hand Tools and Portable Power Tools

## True or False

Directions: Circle T if the statement is True and F if the statement is False.

|  | T | F | A major responsibility of supervisors is to train people in the safe use of hand and portable power tools. |
| --- | --- | --- | --- |
|  | T | F | To reduce the risk of explosion, use spark-resistant tools. |
|  | T | F | A safe way to pass a screwdriver to another person is blade first. |
|  | T | F | Appropriate tool evaluation and selection can reduce tool-related injuries. |
|  | T | F | A screwdriver is a puncture tool. |
|  | T | F | Sharp or pointed tools should be carried in a box or tool belt, not in a pocket. |
|  | T | F | Double-insulated tools can protect against electrical shock. |
|  | T | F | All electric power tools should be effectively grounded unless they are double-insulated or cordless tools. |
|  | T | F | Electrical tools are safest when cords are kept in good condition. |
|  | T | F | An air hose provides power to a pneumatic tool. |
|  | T | F | Keeping track of where company tools are is part of tool control. |
|  | T | F | Two-wire extension cords without grounding are permissible for safe power tool operation. |
|  | T | F | Carrying a tool while climbing a ladder or other structure is safe as long as a worker has full use of one hand. |
|  | T | F | Safe tool practice says to avoid leaving tools on ladders or overhead. |
|  | T | F | One way to control hazards with an electric drill is with personal protective equipment to protect the eyes. |

## Multiple Choice

Directions: Select the best answer and place the corresponding letter in the box provided.

| 2 |  | Which of the following is NOT a general precaution to use with power tools? |
| --- | --- | --- |
|  | A. | Avoid wearing loose clothing or jewelry. |
|  | B. | Use caution when locking the tool to the “on” position. |
|  | C. | Do not operate an electric power tool in a wet location. |
|  | D. | Secure the piece firmly in hand to prevent movement. |

| 2 |  | Which of the following is an example of a torsion tool? |
| --- | --- | --- |
|  | A. | Saw |
|  | B. | Hammer |
|  | C. | Clamp |
|  | D. | Wrench |

| 2 |  | The best way to control tool incidents is: |
| --- | --- | --- |
|  | A. | Eliminating double-insulated tools. |
|  | B. | Conducting regular tool inspections. |
|  | C. | Reviewing incident records. |
|  | D. | Having access to good first aid and medical facilities. |

| 2 |  | A screwdriver should never be used for electrical work unless: |
| --- | --- | --- |
|  | A. | It is too short to cause contact with live parts. |
|  | B. | More than one employee is present. |
|  | C. | It is insulated and approved for electrical work. |
|  | D. | It has a square shank. |

| 2 |  | A tool safety program includes: |
| --- | --- | --- |
|  | A. | Evaluating tools for purchase. |
|  | B. | Training in tool use. |
|  | C. | Procedures for inspection and maintenance. |
|  | D. | All of the above. |

| 2 |  | Precautions for power tools include: |
| --- | --- | --- |
|  | A. | Being aware of the cord location. |
|  | B. | Securing the work piece. |
|  | C. | Using appropriate PPE. |
|  | D. | All of the above. |

| 2 |  | Protection from electrical shock is provided by: |
| --- | --- | --- |
|  | A. | Ground-fault circuit interrupters. |
|  | B. | Extension cords. |
|  | C. | Two-pronged plugs. |
|  | D. | All of the above. |

| 2 |  | Which of the following is an appropriate source of power for an internal combustion portable power tool? |
| --- | --- | --- |
|  | A. | Compressed air |
|  | B. | Gasoline |
|  | C. | Electricity |
|  | D. | Gunpowder |

| 2 |  | Which of the following is NOT a good safety practice for a screwdriver? |
| --- | --- | --- |
|  | A. | Checking the tool before use to see if it is in good repair. |
|  | B. | Using the right driver for the job. |
|  | C. | Using the screwdriver as an impact tool. |
|  | D. | Using a screwdriver with an insulated handle. |

| 2 |  | Which of the following is NOT a good safety practice for electric powered hand tools? |
| --- | --- | --- |
|  | A. | Using a double-insulated tool. |
|  | B. | Using a tool with a three-prong plug. |
|  | C. | Using a tool in conjunction with a GFCI. |
|  | D. | Using a grounded tool with a two-prong plug. |

## Chapter 14: Hand Tools and Portable Power Tools

## Answer Key

1.	T

2.	T

3.	F

4.	T

5.	F

6.	T

7.	T

8.	T

9.	T

10.	T

11.	T

12.	F

13.	F

14.	T

15.	T

16.	D

17.	D

18.	B

19.	C

20.	D

21.	D

22.	A

23.	B

24.	C

25.	D