## Slide 1: CHAPTER 5
Occupational Exposure Limits and Assessment of Workplace Chemical Risks

## Slide 2: Learning Objectives
Describe how occupational exposure limits (OELs) are used in workplace risk assessment.
Identify the key components of an OEL.
Identify the OELs created by various organizations.
Outline the process of OEL derivation.
Apply available information to working conditions to assess hazardous exposure levels.

## Slide 3: Role of OELs In Workplace Risk Assessment
Hazard characterization
Dose-response assessment
Exposure assessment
Risk characterization

## Slide 4: Importance of OELs
Provide a scientific basis to evaluate existing exposure control technologies and to identify worker health and medical surveillance needs
Promote risk communication by informing workers of potentially adverse health effects of chemical exposure
Provide a benchmark for exposure assessment comparisons

## Slide 6: OEL Elements
Concentration units
Recommended Time Weighted Average (TWA)
Additional notations

## Slide 8: Short-Term Exposure Limit (STEL)
A time-weighted average exposure limit whose averaging time is short
In most organizations, a STEL is a 15-minute TWA exposure limit, although other averaging times can be specified for a given chemical.

## Slide 9: Ceiling Limit
A maximum exposure, or ceiling limit that should not be exceeded at any time during the workday

## Slide 10: Hazard Notations
Additional factors may affect the interpretation or use of OELs such as
  toxicity via skin absorption
  potential for sensitization
  carcinogenicity

## Slide 11: Fundamentals of OEL Derivation
Define the scenario and develop the problem formulation.
Gather and summarize the scientific literature.
Select a dose point that will protect workers from the chemical’s toxic effect.
Perform extrapolations to increase the relevance of the point of departure:
  Adjust for route of exposure and exposure duration/patterns using default assumptions on rates of ingestion/inhalation or physiologically based pharmacokinetic (PBPK) models.
  Perform animal-to-human extrapolations and human variability extrapolations
  Apply any additional uncertainty factors
Submit the value for external review.

## Slide 12: No Observable Adverse Effect Level (NOAEL)
The highest dose that does not cause an adverse effect

## Slide 13: Lowest Observable Adverse Effect Level (LOAEL)
The lowest dose that causes an adverse effect

## Slide 14: Point of Departure (POD)
The NOAEL or LOAEL that best identifies the boundary of the onset of adverse effects is selected for OEL derivation