## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Part III: Recognition of Hazards
Chapter 10:
Ionizing Radiation
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
Ionizing radiation is a general term used to refer to those particles energetic enough to knock electrons out of their orbits, generating ions in the process.
  electron volts (eV)
    kinetic energy gained by an electron falling through a potential of 1 volt
  absorbed dose (ergs/gram)
    the amount of energy ionizing radiation deposits in a target material (energy per mass)
      health risk is proportional to absorbed dose

## Slide 3: Ionizing Radiation Sources
Producers of ionizing radiation are commonly referred to as sources, some of which are natural and some man-made.
  cosmos
    magnetic field (exposure higher at poles)
    atmosphere (exposure higher at high elevations)
  radioactive materials
    unstable forms of elements
    radiation-producing machines
  nuclear reactors
  nuclear weapons and testing
    immediate release and fall-out

## Slide 4: Radiation v. Radioactivity
These terms have different meanings, and it is important for the safety professional to understand the difference.
  radioactivity: describes the characteristics of a material as having an unstable nucleus that decays, releasing ionizing radiation
  radiation: energy and/or energetic particles released from a source

## Slide 5: Production of Radioactive Material
There are several processes by which non-radioactive elements may become radioactive.
  activation: bombarding something that is not radioactive with ionizing radiation
  fission and spallation
    Fission: breaking up of atoms in a reactor
    Spallation: breaking up of atoms in non-reactor settings
  contamination: spilling radioactive material onto something else (e.g., fall-out)
      if radioactive contamination can be removed, the item will no longer be radioactive

## Slide 6: Linear Energy Transfer
    Linear energy transfer (LET): The amount of energy ionizing radiation deposits per unit distance.
  range: the distance travelled from its source until the particles have lost so much kinetic energy that they are no longer able to ionize materials.
    range depends on:
      mass and charge of the particle
      energy of the particle
      material through which it is travelling
    high LET vs. low LET
      Ionizing radiation with a high LET deposits its energy rapidly, thus, it has a short range.

## Slide 7: Types of Radiation
Directly ionizing
  alpha particles
    two protons and two neutrons (++)
    high LET
    shielding provided by a short distance of air, sheet of paper, epidermis
      can provide a lethal dose if inhaled or ingested
  beta particles
    electrons (-) and positrons (+)
    low LET
    shielding provided by moderate thickness of plastic or aluminum
    primarily an internal radiation hazard
      can penetrate the skin and lens of the eye
      can produce Bremsstrahlung
      secondary radiation in the form of x-rays

## Slide 8: Types of Radiation (cont.)
  protons (+)
    low LET
      near end of path through a material, it deposits a relatively large amount of energy (high LET)
        Bragg Peak
    major component of cosmic radiation
    very difficult to shield

## Slide 9: Types of Radiation (cont.)
Indirectly ionizing
  neutrons (no charge)
    high LET
    may cause some encountered nuclei to break apart (spallation)
      resulting in emission of positive ions
    may undergo other reactions
      resulting in emission of alphas, protons, more neutrons
    difficult to shield; need thick layer of high-hydrogen content material (e.g., water, paraffin, concrete)

## Slide 10: Types of Radiation (cont.)
  ionizing electromagnetic radiation
    gamma rays and x-rays
    description of EMR
      wave theory
      particle theory (photons)
    the more energetic the radiation, the shorter its wavelength and the higher its frequency
      visible light ranges from 700 nm (red) to 400 nm (violet)
      at wavelengths <300 nm, EMR begins to be capable of producing ionization
    requires lead shielding

## Slide 11: Radioactivity
Radioactive materials have some characteristics that present special safety challenges:
  cannot be switched on or off
  each radioisotope decays at its own rate (can’t be changed)
  radioactive materials occur naturally and are everywhere
  behave biologically identical to non-radioactive isotopes
  are in a dispersible form when created artificially
  human activities can increase exposures

## Slide 12: Half-Life
Half-life: The time it takes for half of the unstable nuclei of a radioisotope to decay to a different isotope (t1/2(phys)).
  a long half-life does not automatically make a radioactive material more of a hazard
  radiation dose a person can receive is what matters
  becquerel (Bq)
    the SI unit of radioactivity
    one radioactive decay per second

## Slide 13: Effects of Radiation on the Body
All humans contain radioactive substances in their bodies.
  The fact that a substance is radioactive does not affect how it is transported or used inside a plant or animal.
  A radioactive substance that is taken in may be:
    promptly exhaled or excreted
    trapped in the lungs
    distributed fairly uniformly throughout the body
    concentrated in one or more particular organs

## Slide 14: Radioactive Materials in the Body (cont.)
  biological half-life (t1/2(bio))
    time it takes for half of any substance to be eliminated from the body as a result of natural biological processes
  effective half-life (t1/2(eff))
    the time it takes for half of any radioactive substance to be eliminated from the body as a result of radioactive decay and natural biological processes
    shorter than the physical half-life or biological half-life

## Slide 15: Radiation Health Effects
  Deterministic effects: Health effects that all individuals will experience if the dose is large enough.
      once the threshold for the effect has been exceeded, the severity depends on the magnitude of the agent
  Stochastic effects: Health effects that only some individuals (pre-disposed) will experience.
      the risk of developing a particular condition or disease increases with increasing exposure to an agent

## Slide 16: Radiation Biology
  relative biological effectiveness
    how effective a particular type of radiation is at producing a specific biological outcome (e.g., sterilizing instruments, causing lung cancer)
  quality factor
    used in radiation protection standards to allow the use of a single set of ionizing radiation limits, regardless of the type of ionizing radiation

## Slide 17: Radiation Biology (cont.)
  tissue dose weighting factor
    takes into account whether an individual received a total-body uniform dose, or if only certain organs were irradiated

## Slide 18: Quantifying Radiation
External Radiation Sources
  dose equivalent
    identical doses of two different types of radiation may cause different health impacts
      (this is where the radiation quality factor comes in)
    deep dose equivalent (≥1 cm deep exposures)
    lens dose equivalent (eye exposures)
    shallow dose equivalent (skin exposures)

## Slide 19: Quantifying Radiation (cont.)
Internal + External Radiation Sources
  committed dose equivalent
    the total dose equivalent delivered to a particular organ or tissue in the 50 years following the intake of the radioactive material
  committed effective dose equivalent
    takes takes into account which body tissues or organs receive the radiation
      (this is where the tissue dose weighting factor comes in)

## Slide 20: Detection and Measurement of Radiation
dosimeters
  used for passive monitoring of personnel and areas
    film badges, pen dosimeters, luminescent badges
  multiple dosimeters may be placed on different body parts
liquid scintillation counters
  used to check for contaminations (wipes)
bioassays
  assess ingestion/inhalation through urinalysis, fecal analysis, etc.

## Slide 21: Detection and Measurement of Radiation (cont.)
gamma spectroscopy
  examines the energies of detected photons to identify radionuclides
Geiger-Mueller counters
  used to detect photons and electrons
  usually calibrated for a single radiation type

## Slide 22: Radiation Standards
scientists and advisory groups
  Regulatory agencies worldwide base their radiation dose limits on the work of scientists and advisory groups.
    Continually revising and updating their recommendations on:
      dose determination methods
      appropriate weighting factors
      dose limits

## Slide 23: Radiation Regulatory Agencies
Complicated framework in the United States
  different regulations depending on:
    location
    facility/activity type (e.g., research, power production, medicine, transport)
    kinds of radiation sources present
    quantities of sources present
  different agencies involved:
    Nuclear Regulatory Commission (NRC)
    Environmental Protection Agency (EPA)
    Occupational Safety and Health Administration (OSHA)
    Department of Transportation (DOT)
    others

## Slide 24: Radiation Regulations
Occupational doses
  much consistency in the United States
Radiation safety standards also include requirements for:
    registration and licensing of radiation sources
    radiation monitoring
    testing of safety features on containers
    incident reporting
    shipping and disposal of radioactive materials
    training
    security
    labeling
    record-keeping

## Slide 25: Radiation Protective Measures
U.S. regulations stress the goal of keeping radiation doses as low as reasonably achievable (ALARA).
  Three factors are critical to reducing dose levels:
      time
        halving the exposure time halves the dose
      distance
        increasing the distance between a person and the source decreases the dose (inverse square law)
      shielding
        best material for shielding should be evaluated on a case-by-case basis