## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Chapter 31:
International Developments in Occupational Safety
and Health
Compiled by David May,
Associate Professor, Safety and Occupational Health Applied Science
Keene State College

## Slide 2: Globally Harmonized System of Classification and Labeling of Chemicals (GHS)
Needed because of
  significant global trade in chemicals
  critical hazard information missing depending on source
  inconsistent approaches for classifying chemicals
  varying definitions of important definitions (e.g., flammables, carcinogens)
  inconsistent recommendations for protecting workers

## Slide 3: History of GHS
Mandate: United Nations Conference on Environment and Development; 1992 (Earth Summit)
Available for implementation – 2003 (“Purple Book”)
  Published by the United Nations
  UN Subcommittee on the Globally Harmonized System of Classification and Labeling of Chemicals maintains and oversees implantation around the world
USDOL/OSHA GHS Final rule promulgated 2012
  Phased-in compliance dates (through 2015)

## Slide 4: Additional Domestic Harmonization
US DOT – transportation of dangerous goods
EPA – labeling of pesticides
CPSC (chemicals in consumer products)

## Slide 5: GHS Design/Basis
Based on hazard assessment
  i.e., the intrinsic hazardous properties of the chemical
Not risk-based
  acceptable risk must be determined by user counties and application situations

## Slide 6: GHS Provisions
Scope: covers all chemicals in all usage situations
  i.e., no exemption of certain classes of chemicals (e.g. pesticides)
Products may be covered in some parts of the life cycle of the but not others (e.g. pharmaceuticals)
Chemical manufacturer or importer responsible for evaluating hazards

## Slide 7: Hazard Classification
Classification criteria
  Physical hazards
  Health and environmental hazards

## Slide 8: Physical Hazards
Explosives
Flammability – gases, aerosols, liquids, solids
Oxidizers – liquid, solid, gases
Gases under pressure
Aerosols
Notes: Focal Point: UN Committee of Experts on Transport of Dangerous Goods, in cooperation with the ILO.

## Slide 9: Physical Hazards (cont.)
Self-Reactive Substances and Mixtures
Pyrophoric – liquids, solids
Self-Heating substances and mixtures
Organic peroxides
Corrosive to metals
Water-activated flammable gases
Notes: Focal Point: UN Committee of Experts on Transport of Dangerous Goods, in cooperation with the ILO.

## Slide 10: Health Hazards
    Acute Toxicity
    Skin Corrosion/Irritation
    Serious Eye Damage/Eye Irritation
    Respiratory or Skin Sensitization

## Slide 11: Health Hazards (cont.)
    Germ cell mutagenicity
    Carcinogenicity
    Reproductive toxicity
    Target organ systemic toxicity – single and repeated dose
    Aspiration hazards

## Slide 12: Environmental Hazards
Hazardous to the Aquatic Environment
Hazardous to the Ozone Layer

## Slide 13: Forms of Hazard Communication
  Labels
  Safety Data Sheets (SDS)
  Training

## Slide 14: Key Label Elements
    Hazard pictograms
    Signal words
    Hazard statements
    Precautionary information
    Product identifier
    Supplier identifier
    Chemical identity

## Slide 15
GHS Pictograms

## Slide 16: Signal Words
“Danger” or “Warning”
  Used to highlight the hazard and discriminate between levels of hazard

## Slide 17: Hazard Statements
A single harmonized hazard statement for each level of hazard within each hazard class
  Example: Flammable liquids
    Category 1: Extremely flammable liquid and vapour
    Category 2: Highly flammable liquid and vapour
    Category 3: Flammable liquid and vapour
    Category 4: Combustible liquid

## Slide 18: Precautionary Statements
GHS label should include appropriate precautionary information (examples of precautionary statements are found in the GHS document ).
Currently the statements are flexible, but the intent is to harmonize precautionary statements in the future.

## Slide 19: Role of the SDS in the GHS
The SDS should provide comprehensive information about a chemical substance or mixture.
Primary use: the workplace
Employers and workers use the SDS as a source of information about hazards and to obtain advice on safety precautions.

## Slide 20: SDS Format: 16 headings
Identification
Hazard(s) identification
Composition/information on ingredients
First-aid measures
Fire-fighting measures
Accidental release measures
Handling and storage
Exposure control/personal protection

## Slide 21: SDS Format: 16 headings (cont.)
Physical and chemical properties
Stability and reactivity
Toxicological information
Ecological information
Disposal considerations
Transport information
Regulatory information
Other information

## Slide 22: Training
Training is necessary to implement GHS system, but provisions are not harmonized.
  In the United States see: OSHA’s Hazard Communication standard for training requirements

## Slide 23: Control Banding
Attempts to address the risk assessment of 100,000s of chemicals without occupational exposure limits (OELs)
Qualitative approach to assess chemical risk and select appropriate control measures
Attributed to the pharmaceutical industry and United Kingdom’s COSHH Essentials

## Slide 24: Control Banding (cont.)
Risk based on chemical hazards and potential for exposure
Utilized risk phrases (R-phases); now harmonized with GHS (Hazard Statements or H-Statements)

## Slide 25
Selection of Four Control Strategies
Control Banding (cont.)
Source: http://www.coshh-essentials.org.uk/

## Slide 26: REACH
Registration, Evaluation, Authorization, and Restriction of Chemicals
Enacted as E.U. regulations concerning importing and selling of chemical products in Europe
Covers complete life-cycle of product

## Slide 27: REACH Requirements
Registration of substances
Detailed evaluation of hazards posed by substance
Substances can be restricted or prohibited if risk is unacceptable
Obligates downstream users to implement conditions of use from suppliers

## Slide 28: REACH Requirements (cont.)
Technical dossier and/or chemical safety assessment depending on quantity of substance manufactured or imported
Risk characterization: Derived No Effect Levels (DNELs) determined for substances used to Predicted No Effect Concentration (PNEC)
Exposure Assessment: Exposure scenarios developed for specific set of operational conditions for downstream users

## Slide 29: Occupational Health and Safety Management Systems (Examples)
Voluntary Protection Program (VPP)
ANSI Z-10 (Occupational Health and Safety Management Systems)
ISO 14000 (environmental management system)
BSI Occupational Health and Safety Assessment Series 18000