## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Chapter 11:
Non-Ionizing Radiation
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
One hallmark of the technological change since WWII has been the increasing use of the electromagnetic spectrum.
  electric fields
    polarity
    electric force
      amount of charge
      polarity of charge
      distance between
  magnetic fields
  electric current

## Slide 3: Current Flow
The amount of charge flowing past a given point in a defined period of time can be described:
  Ohm’s Law
    resistance
    V = I × R
      (voltage equals current times resistance)
    P = V × I
      (power equals voltage times current)
  Joule’s Law
    power
    P = R × I2
      (power equals resistance times the current squared)

## Slide 4: Electric Power Transmission
Generation
Transmission (generating plant to substation)
Distribution (substation to end-user)
Power grid
  direct current (DC) - Edison
    transmitted at same voltage as used (separate lines needed)
    power losses (need high voltage + low current)
  alternating current (AC) - Tesla
    transformers
      step-up (at generation facility) and step-down (distribution/ end-user)

## Slide 5: Electric Power Transmission (cont.)
Transmission lines
Conductor size
  Pouillet’s Law
    resistance increases with increasing length
    resistance decreases with increasing cross-sectional area
    aluminum-conductor steel-reinforced (ACSR)

## Slide 6: Electromagnetic Radiation
Electromagnetic radiation: describes the phenomenon where both electric and magnetic fields exist together.
  frequency (f)
    number of times a field reverses polarity (60 Hz)
  wavelength (λ)
    distance a wave travels in one cycle
    Note: frequency × wavelength = speed of light (186,000 mi/sec)
      if f, then λ must
      if f, then λ must

## Slide 7: Electromagnetic Spectrum
    The electromagnetic spectrum spans an immense range of frequencies.
    Four types of radiation based on energies:
    subradio 0 – 3 kHz
    radio/microwave 3 kHz – 300 GHz
    optical 300 GHz – 3 × 1015 Hz
    ionizing > 3 × 1015 Hz
    measured in milliwatts of power per square centimeter of area (mW/cm2)
      power density
      irradiance

## Slide 9: Near and Far Fields (What to Measure)
Separate electric and magnetic fields are commonly found at lower frequencies (longer wavelengths).
Radiation is commonly found at higher frequencies.
  near fields
    reactive near fields (λ > 1 m, 300 MHz)
      electric fields and magnetic fields found
    radiating near fields (λ < 1 m, 300 MHz)
      electric and magnetic fields combine to form radiation
  far fields
      only radiation found

## Slide 10: Parts of Electromagnetic Devices
  Any electromagnetic device can be visualized as having three parts:
    source
    transmission pathway
    receiver
  Particular attention should be paid to the “transmission pathway” since it represents opportunities for worker exposure.

## Slide 11: Measuring Field Strengths
  electric fields
    displacement sensor (dipole antennae)
      pair of flat plates inserted into the field
      measure electric potential between the plates
  magnetic fields
    magnetometer
      contain loops of conducting wire
      magnetic flux induces a current
      can be ganged to become omni-directional

## Slide 12: Biological Effects of Steady Fields
  DC electric fields (do not change polarity)
    sparks (irritating @ 5 kV/m, painful @ 15 kV/m)
    TLVC is 25 kV/m
  Magnetic fields
    nausea
    metallic taste
    dizziness
    flashes in eyes
    TLV 8-hr TWA is 2 tesla (T)

## Slide 13: Biological Effects of Time-Varying Fields
Subradiofrequency Fields
  possible human carcinogen
  influence on cell membrane transport
  circadian rhythm
Classic safety concerns
  effects on cardiac pacemakers
  movement of magnetized tools and equipment
  wiping of magnetic media (e.g., discs, credit cards, hard drives)

## Slide 14: Health Regulation Criteria
    Difficult to establish—does not follow linear dose-response models.
    exposure criteria
      amount of individual exposure
    emission criteria
      how much can be released
      prudent avoidance (similar to ALARA for ionizing radiation)
      precautionary principle (limit exposures to extent practical)

## Slide 15: Subradiofrequency/Microwave Shielding
  Electric fields
    use of conductive screens/sheets with attached grounding conductor (mesh < ¼ λ)
  Magnetic fields
    permeable alloy to confine magnetic flux lines into shield material and around shielded area
    active shielding (field cancellation)
      uses an electric coil system and feedback controls to generate opposing fields
      Note: This happens unintentionally with household wiring.
      Current flows in one direction through wire and the returning current flows in opposite direction through an adjacent wire.

## Slide 16: Biological Effects of Time-Varying Fields
  Radiofrequency/Microwave
  some scenarios involve fields and others involve radiation
  absorption, scatter, transmission, reflection
  dosimetry
    The response of tissue to radiation and fields is determined by the electrical properties of the tissue
    size of organism
      40% λ and ungrounded, 20% λ and grounded
    polarization of radiation
      electric field parallel to long axis of organism
    interaction of exposed tissue
      specific absorption rate (SAR)

## Slide 17: Biological Effects of Radiofrequency
Some scenarios involve fields and others involve radiation.
    Only proven adverse human effects are eye cataracts, facial burns, and electric shocks and burns
    Standards specify exposure limits for 6-minute intervals.
      see ANSI/IEEE C95.1-2005 – incorporated by reference by OSHA
    Sub-resonant Region (<3 MHz)
      goal of standard is to prevent burns and excessive ankle heating
    Resonant Region (3 MHz to 6 GHz)
      peak absorption for humans occurs at 30 to 300 MHz
      current flow and SAR both important considerations
    Super-resonant Region (> 15 GHz)
      skin absorption predominates (thermal damage to skin)

## Slide 18: Radiofrequency/Microwave Controls
shielding
  absorbing foams
  metal screens or sheets (Faraday cages)
waveguides and coaxial cables
distance
  far fields (inverse square law)
  near fields (barricades, long-handled tools)
time limitation
  based on 6-minute averaging time
signage

## Slide 19: Biological Effects of Optical Radiation
  Optical radiation includes IR, visible, and UV radiation.
    The lens of the eye transmits visible and IR-A radiation but absorbs other IR bands and UV radiation.
  eyes
    thermal effects (IR)
    photochemical effects (UV)
  skin
    skin toughening (UV-B)
    skin cancer (UV-C)
    Note: Exposure standards found in
    ACGIH TLV booklet. Major concerns at frequencies < 1.4 μm due to retinal focusing.

## Slide 20: Visible (Non-Laser) Controls
optical density
  log10 of intensity of light leaving a filter v. entering the filter
  if filter absorbs all but 1%: (1% = 1/100, log10 of 100 = OD 2)
shade factor
  variation of optical density used in ANSI A49.1 for welders
  shade number = 1 + (2.33 × OD)
optical baffles and sight barriers
  engineering controls
personal protective equipment
  regular glass (UV-B and UB-C)
  tinted glass (UV-A)
  eye protection PPE must be distinctly marked

## Slide 21: Biological Effects of Laser Radiation
Laser radiation has unique properties:
  monochromatic (only one color/wavelength of light)
  coherent (all waves in phase)
  bright (very high irradiance, focused)
  results in injury through:
    thermal burns
    photochemical effects
    thermoacoustic tissue damage
      brightness striking retina may be 300,000 times greater than that entering the eye
      blood is toxic to nerve tissue

## Slide 22: Laser Controls
Engineering and administrative controls and PPE are used for lasers.
  engineering controls
    enclosure
    routing
    fail-safe interlocks
    remote interlock connections
    key-in-lock control
  administrative controls
    exclusion (barriers, signs, beacons)
    medical surveillance programs
    training programs
  personal protective equipment (PPE)
    necessary to match optical density to wavelengths encountered

## Slide 23: Non-Beam Hazards of Lasers
electricity (high-voltage currents, capacitor banks)
fire
  ignition source
  toxic pyrolysis products
  carcinogenic polycyclic aromatic hydrocarbons (PAHs)
lacerations (exploding flash lamps)
biological (in plumes when used for cutting tissues)
toxicity/mutagenicity (original dyes used DMSO)
corrosiveness (gases used)
other radiation (electromagnetic fields, x-rays)
hazardous materials (heavy metals in detectors, heat sinks)

## Slide 24: Laser Standards
  Control class regulations—precautions become more stringent in a series of defined steps.
  Class 1: extremely weak; intrinsically safe; no precautions needed
  Class 2: low-power; hazardous if prolonged viewing; limited precautions
  Class 3: moderate-power; hazardous if viewed briefly; more precautions
  Class 4: high-power; harmful if glimpsed; rigorous precautions
  Laser Institute of America
    LIA/ANSI Z136.1-2007 (dominant standard)
  Food and Drug Administration
    standards for commercial laser products
  OSHA
    standard for construction workers