## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Chapter 12:
Thermal Stress
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: Introduction
Thermal stress is a significant physical agent in many workplace environments.
Just considering routine out-of-doors work, air temperatures ranging from -20°F to 110°F can reasonably be expected in many places throughout the United States.

## Slide 3: Degrees of Thermal Stress
Conceptually, work can occur in one of five zones along the continuum of thermal stress:
  heat health risk zone
  heat discomfort zone
    physiological adaptions great
    behavioral adaptations modest-to-great
  comfort zone
    physiological adaptations modest
    behavioral adaptations minor
  cold discomfort zone
    physiological demands great
    behavioral adaptations modest-to-great
  cold health risk zone

## Slide 4: Model of Thermal Balance
Three factors influence the degree of thermal stress:
  climatic factors
    air temperature, relative humidity, wind chill
  work demands
    substantial contributor to heat gain
  clothing
    insulation (resistance to heat flow)
    permeability (water vapor movement)
    ventilation (air movement)
  chimney effect + bellows effect

## Slide 5: Model of Thermal Balance (simplified)
  S = M + R + C – E
  where: S = heat storage rate (gain [+] or loss [-])
  M = metabolic rate (internal heat generation [+])
  R = radiant heat exchange rate (gain [+] or loss [-])
  C = convective heat exchange rate (gain [+] or loss [-])
  E = evaporative heat loss (always loss [-])

## Slide 6: Heat Stress
A combination of factors tends to increase body temperature, heart rate, and sweating.
  The physiological adaptations to heat stress are known as heat strain.
  core body temperature
  heart rate
  sweat rate
    acclimation
    adaptive working (pacing)

## Slide 7: Recognition of Heat Stress
Heat stress in the workplace can be recognized in terms of:
  workplace risk factors
    hot or humid environments
    high work demands
    protective clothing requirements
  effects on workers
    low-end: worker behaviors (shedding clothes, work pacing)
    middle: redness of face/skin, profuse sweating, rapid breathing
    high-end: heat-related disorders (nausea, cramps, heat exhaustion)

## Slide 8: Heat-Related Disorders
    Heat-related disorders are the manifestations of over-exposure to heat stress.
  see Table 12–A in text for information on:
    signs a trained observer may see
    symptoms a worker may report
    likely causes of the disorder
    first aid
    steps for prevention
  physiological markers
    measuring temperature (100.4°F)
    measuring heart rate (< 110 bpm average or < 160 bpm)
    measuring water loss (> 1.5% loss of body weight)

## Slide 9: Worker Behaviors
Heat stress not only induces physiological changes, but also affects behavior:
  actions that reduce exposures
    adjusting clothing to increase evaporative losses
    slowing work rate
    taking small breaks
    taking shortcuts in work methods
  changes in attitudes
    irritability
    low morale
    absenteeism
  unsafe acts
    increased number of errors
    increased number of machine breakdowns
    taking short cuts in work methods

## Slide 10: Evaluation of Heat Stress
  The World Health Organization set the tone for worker protection in 1969.
  forms the basis for NIOSH and ACGIH heat stress guidelines
    long-duration exposures
      core temperatures should not exceed 100.4°F
    short-duration exposures (with recovery periods)
      core temperatures should not exceed 102.2°F
    average heart rate
      not over 110 bpm

## Slide 11: ACGIH® TLV ® for Heat Stress
  Recognizes the difference between eight-hour and short-duration exposures.
  assessment of metabolic rate
    basal metabolism
    posture
    activity (based on body movement)
    horizontal travel
    vertical travel
  assessment of environmental conditions
    air temperature
    humidity
    air speed
    average temperature
  clothing adjustment factor (CAF)

## Slide 12: Control of Heat Stress
  The control of heat stress centers around the causes and their resulting physiological strain.
  Takes the form of:
    general controls
      applicable to all heat-related jobs
    specific controls
      evaluated and selected based on constraints of the working conditions

## Slide 13: Control of Heat Stress (cont.)
General Controls
  training
    pre-placement training
    periodic training
  heat stress hygiene practices
    fluid replacement
    self-determination
    diet
    lifestyle
    health status
    acclimation
  medical surveillance
  evaluation of risk
  response to heat-related disorders
  emergency plan

## Slide 14: Control of Heat Stress (cont.)
Specific Controls
  engineering controls
    reducing physical work demands
    adjusting clothing requirements
    reducing external heat gain
    enhancing external heat loss
  administrative controls
    acclimation
    work-pacing
    work-sharing
    work scheduling
    pre-determined work times
    self-determination
    personal monitoring
personal protection
  circulating air systems
  circulating water systems
  ice garments
  reflective clothing

## Slide 15: Cold Stress
  Cold stress is a fundamentally different kind of problem than heat stress.
  Physiological adaptations to cold stress have less dramatic effects.
Human responses to cold stress
  physiological
    reduced blood circulation to skin
    increased metabolic activity (shivering)
  behavioral
    increased activity
    seeking warm locations
    increased clothing insulation
      insulation value
      moisture
      ventilation

## Slide 16: Cold Stress Hazards
Hazards associated with cold stress are manifested in two distinct fashions:
  systemic (hypothermia)
    depression of central nervous system
  local (localized tissue damage)
    restriction of flood flow to extremities
    Note: There is also a concern for manual dexterity.

## Slide 17: Model of Thermal Balance (simplified)
  S = M + (R + C) + K – E
  where: S = heat storage rate (gain [+] or loss [-])
  M = metabolic rate (internal heat generation [+])
  R = radiant heat exchange rate (gain [+] or loss [-])
  C = convective heat exchange rate (gain [+] or loss [-])
  K = conductive heat exchange (loss [-])
  E = evaporative heat loss (always loss [-])
  Note: The goal of systemic cold-stress control is to avoid hypothermia by limiting reduction in core temperatures to:
  - 96.8°F for prolonged exposures
  - 95°F for occasional, short-duration exposures

## Slide 18: Measurement of Cold Stress
Two climatic factors influence the rate of heat exchange between a person and the environment:
  air temperature
  air speed
    Note: The Wind Chill Index was developed by the National Weather Service to reflect the effect of these variables on heat exchange.

## Slide 19: Recognition of Cold Stress
Subjective responses of workers are a good tool for recognition of cold stress in the workplace:
  seeking warm locations
  adding layers of clothing
  increasing the rate of work
  loss of manual dexterity
  shivering
  accidents
  unsafe behaviors

## Slide 20: Evaluation for Cold Stress
  Workplace monitoring
    should be conducted when temperatures fall below 61°F
  Systemic cold stress
    hypothermia can occur with air temperatures up to 50°F
    ACGIH recommends employers invoke protective measures when air temperatures fall to 41°F

## Slide 21: Control of Cold Stress
General controls
  training
    additional topics for colder exposures
  cold stress hygiene practices
    fluid replacement
      warm, sweet, non-caffeinated
    diet
    self-determination
    wet clothing replacement
  medical surveillance
    medical restriction for those unable to adequately thermoregulate

## Slide 22: Control of Cold Stress (cont.)
Specific Controls
  engineering controls
    general or spot heating
    minimizing air movement
    reducing conductive heat transfer
    provision of warming shelters
  administrative controls
    acclimation
    work/rest cycle
    work-sharing
    work scheduling
    allow for production declines
    avoid long periods of sedentary work
    personal monitoring
  personal protection
    insulated clothing
    wind barriers
    special attention to extremities
      face shields
      gloves/mittens
      socks/footwear
    active warming systems
    eye protection