## Slide 1: CHAPTER 14
Ergonomics

## Slide 2: Learning Objectives
Describe the study and goals of occupational ergonomics.
Identify the signs and symptoms of musculoskeletal injuries.
Recognize and describe the different types of common musculoskeletal injuries and illnesses.
Define various aspects of anatomy and anthropometry as they relate to the study of ergonomics.
Identify categories of contributing risk factors for musculoskeletal hazards.
Understand various methods for assessing and quantifying musculoskeletal risks and hazards in working environments, activities, and conditions.
Develop controls that can minimize or reduce workplace musculoskeletal hazards.
Use the NIOSH lifting equation to analyze working conditions and compare them with lifting guidelines.
Establish an ergonomics workplace safety program and associated training materials.

## Slide 3: Definition of Ergonomics
The study of the relationship among the human body, the human mind, and the physical environment.
Ergonomists evaluate a person’s size, shape, and neural/cognitive abilities and match them to the materials, equipment, structures, tools, and systems the person interacts with.

## Slide 4: Definition of Ergonomics (cont.)
Ergonomics builds upon several core sciences, including anatomy, physiology, mathematics, and physics and incorporates anthropometry, psychology, statistics, biomechanics, and engineering.
The primary goals of ergonomics are to help humans perform tasks more efficiently, be more comfortable, and have fewer injuries.

## Slide 5: Areas of Study
Physical
Cognitive
Organizational

## Slide 6: Musculoskeletal Hazards
Highest rates: health care, transportation and warehousing, retail and wholesale trades, and construction
30 percent of all workers’ compensation claims are for overexertion and repetitive-motion injuries, and claims for these injuries typically occur more than twice as often as those for other workplace injuries.

## Slide 7: Musculoskeletal Injuries
Often difficult to diagnose
Joint pain, numbness, tingling, swelling, restricted motion
Musculoskeletal disorders (MSDs)

## Slide 8
Carpal Tunnel Syndrome
One of the most common musculoskeletal workplace injuries
Source: Blausen.com staff. “Blausen Gallery 2014.” Wikiversity
Journal of Medicine. DOI:10.15347/wjm/2014.010.

## Slide 9
Thoracic Outlet Syndrome
Source: Nicholas Zaorsky, M.D.

## Slide 10: Other Musculoskeletal Injuries
Tendinitis
Tendonitis
Lower back strain
Hand-arm vibration syndrome/white finger syndrome
Trigger finger
Rotator cuff damage
Epicondylitis

## Slide 11
Anatomy

## Slide 12
Source: OpenStax College. “Anatomy & Physiology.” Connexions Web site. http://cnx.org/content/col11496/1.6/, June 19, 2013.
Pronation and Supination

## Slide 13: Capacity for Work

## Slide 14: Musculoskeletal Workplace Hazards
Repetitive/long durations
Awkward postures
Static postures
Excessive force
Vibration
Temperature extremes

## Slide 15: Hazard Assessment
Source: BanksPhotos/iStock
Source: Used with permission
from 3B Scientific.

## Slide 16: Hazard Assessment (cont.)
Source: Agricultural Technology
Research Program at Georgia Tech
Source: EmmaLDavis/Wikimedia
Commons

## Slide 17: Control of Musculoskeletal Hazards
Workplace design
  Fit the job to the worker
  Adjust the work space
  Place work at same level
  Forward Facing
  Reduce the Force
  Improve grip strength
  Use tools to support the task
  Special equipment
Source: Electro Kinetic Technologies

## Slide 18: Control of Musculoskeletal Hazards (cont.)
Administrative controls
  Programs and procedures
  Worker training
  Job site assessment
  Job rotation/shift length/work pace/rest breaks
  Reduce organizational stressors/stress
  Control ancillary hazards (noise, radiation, excessive temperatures, biological, chemical)

## Slide 19: Recommended Weight Limits (RWLs)

## Slide 20
Calculating Multipliers

## Slide 21
Coupling Multipliers

## Slide 22
Frequency Multipliers