## Slide 1: Fundamentals of Industrial Hygiene 6th Edition
Part VI: Evaluation of Hazards
Chapter 15:
Evaluation
Compiled by Allen Sullivan,
Assistant Professor, Safety and Health Management Central Washington University

## Slide 2: General Principles
In 2009, 3.3 million occupational work-related injuries and illnesses occurred in private industry.
  actual number is much larger:
    many occupational illnesses are unrecognized
    many injuries and illnesses are not reported
    public sector not included in the count
Given the weaknesses of the data systems, a focus on evaluation of hazards is even more important.

## Slide 3: General Principles (cont.)
The evaluation of the nature and severity of hazards relies on many factors:
  toxicity;
  exposure levels or dose;
  duration of exposure
  process or operation analysis;
  maintenance activities, spills, and accidents;
  epidemiology and risk assessment;
  interview;
  unequal distribution of risks; and
  variability of response

## Slide 4: Basic Approach to Hazard Recognition
Three-step, systematic procedure:
  consider the raw materials being used
  consider how raw materials are modified during use
  evaluate the finished products and by-products (wastes)
  Note: Should be evaluated under normal conditions and under anticipated emergency conditions.

## Slide 5: Basic Approach (cont.)
Any job can include multiple forms of hazards (physical, chemical, biological).
The evaluator must note each of these, and be aware of possible interactions.
  acute traumatic
    vehicles
    sources of energy
  cumulative, long-term
    work postures
    vibration
    radiation
biological
    infectious agents
    toxins
  psychosocial
    machine pacing
    repetitive tasks
    shift work

## Slide 6: Basic Approach (cont.)
A first step is becoming familiar with typical hazards associated with the industry.
review of literature
  pamphlets, reports, technical bulletins
  industry-sector common violations
  mailing lists, e-newsletters

## Slide 7: Basic Approach (cont.)
Next, a list of all chemicals present in the facility should be developed and reviewed.
  Inventory
    legal standards (OSHA PELs)
    guidelines (NIOSH RELs, ACGIH TLVs)
    Be careful—there are many chemicals for which there is no OEL.
inventory can be expanded to include:
    physical hazards
    ergonomic hazards
    biological hazards
    psychosocial hazards

## Slide 8: Basic Approach (cont.)
Lastly, information about industrial operations is needed to link hazardous materials, their use in production, and worker contact with them.
  Process Description
    quantity of amounts used
    how and where materials are used
    exposure potential
      when
      via what route
      for how long

## Slide 9: Process Flow Sheets
Although chemicals used in closed systems are not normally released into the atmosphere, exposures can arise from:
  leaks
  charging the system
  intentional releases (e.g., sampling points)
  recirculation of stack gases
  accidental releases (e.g., equipment malfunction)
  maintenance and repair activities

## Slide 10: Checklists
A checklist for evaluating environmental hazards arising from industrial operations can be created.
Should be modified to fit each organization’s particular situation.
  overall process or operation
    list all hazardous agents used during the process
  equipment
    list all equipment that contain hazardous materials or energy that could be suddenly released
  cleaning methods
    list all hazardous materials used
    list all contaminants that could be displaced

## Slide 11: Process Safety Management
    29 CFR 1910.119 recognizes that catastrophic releases could occur wherever large quantities of highly hazardous chemicals are used or stored.
  evaluation of potential causes and consequences of:
    fires
    explosions
    releases
    spills
  includes requirements for:
    written operating procedures
    training
    inspection and testing
    safety reviews

## Slide 12: Field Surveys
Evaluation requires on-site and direct observation, measurement, interviews, and interpretation of data:
  walk-through
    follows the flow of material through a facility
    include non-production areas
  sensory perception
    visual, auditory, olfactory
  control measures in use
    engineering, administrative, personal protective equipment
  observation and interview
    observation
    interview

## Slide 13: Monitoring and Sampling
  There are a number of reasons why environmental measurements should be taken in the workplace:
  evaluating degree of worker exposure
  identification of sources for peak exposures
  evaluation of control-measure effectiveness
  compliance with occupational and environmental regulations
  deciding if an area is clear for re-occupancy
  establishing background concentrations
  warning of peak releases

## Slide 14: Monitoring
  Monitoring is a continuous program of observation, measurement, and judgment—it is more than just sampling.
  personal monitoring
    active sampling
    passive sampling
  environmental (area) monitoring
    ambient air sampling
  biological monitoring
    measurement of the contaminant
    measurement of metabolites
    measurement of enzymes or functions that reflect harm
  medical monitoring
    screening, early detection, preventative

## Slide 15: Sampling
  Preliminary research and initial field surveys help identify potential hazards to which workers may be exposed.
  strategy
    worst-case approach
    typical-condition approach
    how it will be used
  what to sample
    should represent workers’ exposures
  how to sample
    time-weighted averages
    grab sampling
    direct-read instruments

## Slide 16: Sampling (cont.)
  where to sample
    personal monitoring
    area monitoring
  whom to sample
    proximity
    work habit
  when to sample
    season-to-season variations
    air-conditioning
    work-shift

## Slide 17: Sampling (cont.)
  how long to sample
    sensitivity of instrument
    estimated air concentration
    OSHA PEL or ACGIH TLV
  what to note while sampling
    fundamental records
    supplemental records
  how many samples to take
    purpose of sampling
    number of tasks performed
    contaminant generation variability

## Slide 18: Sampling (cont.)
  when to stop sampling
    regulated contaminants (ongoing, routine)
    results from most recent sampling (compared to baseline)
  who should conduct sampling
    adequately trained workers
    supervised by professional industrial hygienist
    needs knowledge of:
      potential errors
      proper calibration and maintenance of equipment
      potential problems
      sampling limitations
      how to integrate observations and interviews
      when it is not necessary to sample

## Slide 19: Sampling Accuracy and Precision
To sample means to measure only a part of the environment, and, from the measurements taken, infer conclusions about the whole.
  accuracy
    relationship between measured value and true value
    systematic errors
      method error
      personal error
      instrument error
    consistent bias to results

## Slide 20: Sampling Accuracy and Precision (cont.)
  precision
    degree of agreement among results from repeated measurements
    random errors
      intra- or inter-day concentration fluctuations
      sampling equipment variations
      analytical method fluctuations
    variability among results

## Slide 21: Sampling Accuracy and Precision (cont.)

## Slide 22: Interpretation of Results
  There are times when the interpretation of results is not a completely straightforward process.
  It is always important to keep in mind why the sampling was done:
    compliance
      OSHA PELs
    good practices and worker protection
      ACGIH TLVs and NIOSH RELs

## Slide 23: Limitations of Standards
While any sampling result that is less than the PEL is considered to be in compliance with the law, this shouldn’t be interpreted as a “clean bill of health.”
  only evaluate inhalation exposures (not dermal or ingestion)
  out of date (most based on 1968 TLVs)
  based on inadequate research (do not address chronic toxicity)
  based on white, male workers
  allow a level of risk not tolerated for general environmental exposure
  fail to account for multiple exposures (ignore additive or synergistic)
  fail to offer comprehensive protections (only 10% of chemicals have PELs)
  represent a political compromise (regarding economic feasibility)